| Assessment Number | sUAV-Hooe-2017 |
| --- | --- |

Hazard and Risk Assessment Summary

| School/Dept | EESE |  | Location of Activity | Hooe Lake, Plymouth |  | Date of Assessment | 26/04/2017 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Assessor |  |  | Activity Assessed | Aerial Video survey of inaccessible wrecks |
|  |  |  | (Attach protocols) |  |
| Assessment of Hazard and Risk | Control Measures Required |
| HAZARD (List only hazards from which there is a significant risk of serious harm under foreseeable conditions) | PERSONS AT RISK (See key, | PERSONAL HARM? | LIKELIHOOD of HARM? |  |
|  | Indicate number) | F | Mj | Mn | Y | Pr | Po | R |  |
| Personal injury to non-University Team members caused by loss of control of sUAV (e.g.persons hit by falling UAV or by elements of the sUAV (e.g. propellers). Specific system-related injuries Damage to wrecksite caused by loss of control of UAV (including loss of pilot awareness/pilot error, sudden wind gust, etc.). | S, Pg, V, Pu S, pP, V, Pu N/A Unless debris also impacts observers (see above) | ( X X | ( ( X | X X X | X X X | X X X | X X X | ( ( X | Ensure minimum separation distance of 50m between non-University observers and sUAV flight path/trajectory. Delay or cancel flying until area is clear of members of thepublic. Adhere to guidance laid down in SOP Document SOPs UAV V1.3 (01/2017). Be vigilant for any military aircraft in transit (e.g. Citadel-landing helos). Adhere to sUAV deployment guidance laid down in SOP Document SOPs UAV V1.3 (01/2017). Adhere to sUAV deployment guidance laid down in SOP Document SOPs UAV V1.3 (01/2017). Fly only over the lake area and away from any buildings surrounding the edge. Avoid domestic properties completely. |
| Accident during vehicular transit of sUAV equipment to operational site. | S, Pg | ( | ( | ( | x | x | x | ( | Ensure two drivers and take breaks every two hours. |
| Accident during manual transit of equipment from vehicle to launch site. | S, Pg | x | x | ( | x | x | ( | ( | Ensure appropriate number of personnel available to handle equipment (e.g. Peli cases), adopt correct lifting procedures throughout and take appropriate transit path from vehicle to launch site. Be aware of soft sand/mud conditions of Hooe Lake at low tide throughout. |

| Key | PERSONS AT RISK |  | PERSONAL HARM? |  | LIKELIHOOD |  | Risk Significance | Date for Review | 02/05/2017 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Ug | Undergraduate |  | F | Fatality |  | Y | Yes/ Very High |  |  | Y | Pr | Po | R |  |  |  |  |  |
|  | Pg | Postgraduate |  | Mj | Major Injury |  | Pr | Probable |  | F | ( | ( | ( | ( |  | ( | = Significant risk |  |  |
|  | S | Staff |  | Mn | Minor Injury |  | Po | Possible |  | Mj | ( | ( | ( | ( |  |  |  |  |  |
|  | C | Contractor |  |  |  |  | R | Remote |  | Mn | ( | ( | X | X |  | X | = Insignificant risk |  |  |
|  | V | Visitor |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  | Pa | Patient |  |  | Major Injury: | Loss of or broken limb |  |  |
|  | Pu | General Public |  |  |  | Loss of or damaged eye |  |  |
|  | Yp | Young Person |  |  |  | Loss of consciousness |  |  |
|  | Nm | New/Expectant Mother |  |  |  | Acute illness needing medical treatment | g:\aww7text\guidance\17ra.doc |  |
|  |  |  |  |  |  | Permanent ill health or disability | 19.12.00 |  |