| Assessment Number | sUAV-Waddington-2017-1 |
| --- | --- |

Hazard and Risk Assessment Summary

| School/Dept | EESE |  | Location of Activity | Lincolnshire Urban Search & Rescue Unit (USAR) |  | Date of Assessment | 10/05/2017 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Assessor |  |  | Activity Assessed | Aerial Video Survey (11/05/2017) of USAR Rail Crash Zone for Pix4D 3D recreation (undertaken with the approval and involvement of USAR personnel). |
|  |  |  | (Attach protocols) |  |

| Assessment of Hazard and Risk | Control Measures Required |
| --- | --- |
| HAZARD (List only hazards from which there is a significant risk of serious harm under foreseeable conditions) | PERSONS AT RISK (See key, | PERSONAL HARM? | LIKELIHOOD of HARM? |  |
|  | Indicate number) | F | Mj | Mn | Y | Pr | Po | R |  |
| Personal injury to non-University Team members caused by loss of control of sUAV (e.g.persons hit by falling UAV or by elements of the sUAV (e.g. propellers)). Air Traffic collision/near miss Specific system-related injuries Damage to Goonhilly buildings/airfield assets caused by loss of control of UAV (including loss of pilot awareness/pilot error, sudden wind gust, etc.). | S, Pg, V, C S, Pg, V, C, MoD S, Pg, N/A Unless debris impacts observers (see above) | ( ( X X | ( ( ( X | X X X X | X X X X | X X X X | X X X X | ( ( ( X | Ensure minimum separation distance as defined in SOPs between non-University observers and sUAV flight path/trajectory. Delay or cancel flying until area is clear. Adhere to guidance laid down in SOP Document SOPs UAV V1.3 (01/2017). Discuss flight plans with USAR and accompanying MoD personnel, especially wrt flights in close proximity to RAF Waddington (MoD to liaise with ATC). Although the airspace over RAF Waddington is a “no-fly” zone, be aware of aircraft (rotary/fixed-wing/UAV) movements into and out of the airfield and cancel flight/land as soon as possible. Contact has been made with RAF Waddington Air Ops and they are happy for the flying to happen. Start and end times must be telephoned in to the ATC Tower (via accompanying MoD representative). Adhere to sUAV deployment guidance laid down in SOP Document SOPs UAV V1.3 (01/2017). Adhere to sUAV deployment guidance laid down in SOP Document SOPs UAV V1.3 (01/2017). |
| Accident during vehicular transit of sUAV equipment to operational site. | S, Pg | ( | ( | ( | X | X | X | ( | Ensure driver takes breaks every two hours. |
| Accident during manual transit of equipment from vehicle to launch site. | S, Pg | x | x | ( | x | x | ( | ( | Ensure appropriate number of personnel available to handle equipment (e.g. main Peli case), adopt correct lifting procedures throughout and involve Goonhilly personnel regarding appropriate transit path from vehicle to launch site. |
| Key | PERSONS AT RISK |  | PERSONAL HARM? |  | LIKELIHOOD |  | Risk Significance | Date for Review | 12/05/2016 |
|  | Ug | Undergraduate |  | F | Fatality |  | Y | Yes/ Very High |  |  | Y | Pr | Po | R |  |  |  |  |  |
|  | Pg | Postgraduate |  | Mj | Major Injury |  | Pr | Probable |  | F | ( | ( | ( | ( |  | ( | = Significant risk |  |  |
|  | S | Staff |  | Mn | Minor Injury |  | Po | Possible |  | Mj | ( | ( | ( | ( |  |  |  |  |  |
|  | C | Contractor |  |  |  |  | R | Remote |  | Mn | ( | ( | X | X |  | X | = Insignificant risk |  |  |
|  | V | Visitor |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  | Permanent ill health or disability | 19.12.00 |  |